## Slide 1
Raspberry Pi
Raspberry Pi Line following Robot Car Wiring Connections
Right Infrared Sensor
Pi’s Micro USB Power Connection
USB Portable mobile phone charger
L298N
+12v Gr +5 v
1 2 3 4
L298N Motor Controller
Left DC motor
GPIO 15
GPIO 13
Right DC motor
OUT
VCC
GND
Left Infrared Sensor
OUT
VCC
GND
GPIO 14
4 6 8 10 12 14 16 18 20 22 24
2
GPIO 10
GPIO 2
1 3 5 7 9 11 13 15 17 19 21 23
GPIO 9
GPIO 4
GPIO 7
GPIO 6
A. Davis issue 1.0 19.02.2015

## Slide 2
L298N
+12v Gr +5 v
1 2 3 4
L298N Motor Controller
Raspberry Pi
A. Davis issue 1.0 19.02.2015
Chassis View
Front
GND
OUT
23 21 19 17 15 13 11 9 7 5 3 1
GND
OUT
Right Infrared Sensor
Left Infrared Sensor
Right DC motor and wheel
Left DC motor and wheel
Raspberry Pi Line following Robot Car Wiring Connections
24 22 20 18 16 14 12 10 8 6 4 2
Pin 15
Pin 13
Forward
Forward
Left Sensor | Right Sensor | Left Motor | Right Motor
On | On | On | On
Off | Off | Off | Off
On | Off | On | Off
Off | On | Off | On

## Slide 3
Line Following PiBot List of Parts
Device | Website
Raspberry Pi (any version) | Search on Amazon for Raspberry Pi
L298N Motor Controller | Search on Amazon for Raspberry L298N Motor Driver
2WD Beginner Robot Chassis | Search on Amazon of robot chassis kit
GM3 gear motor x 2 | https://www.robotshop.com/uk/solarbotics-gm3-gear-motor-3.html
GMPW wheels x 2 | https://www.robotshop.com/uk/solarbotics-gmpw-gm-plastic-wheel.html
Infrared Sensors | Search on Amazon for Obsidian 5V Infrared Line Track Tracking Tracker Sensor
Battery holder for 4 AA’s | Should come as part of the Robot Chassis kit
4 AA batteries | Any supermarket
Portable mobile phone charger | Search on Amazon for Bonai Portable Phone Charge
USB Power cable | Search on Amazon for USB cable for samsung
Ribbon cable | Search on Amazon for ribbon cable